## Slide 1: PCIe Boot
Fadu Andy
Fadu Lucia

## Slide 2: 목적
NVMe device에 PCIe boot를 이용해서 Mkbootimg로 생성한 Image를 fusing 하는 것
PMU
ROM Code
Fuser.bin
nvme_ddr.bin
FW.bin
Load
Load & Run
Load & Fusing

## Slide 3: PCIe_Boot Usage
Usage
  python pcie_boot.py –h
  python pcie_boot.py (default : --dev_bdf 01:00.0 --ddr ddr.bin --fuser fuser.bin --fw fw.bin)
    Ex. python pcie_boot.py
    Ex. python pcie_boot.py --dev_bdf 02:00.0
    Ex. python pcie_boot.py --dev_bdf 02:00.0 --ddr ddr2.bin
    Ex. python pcie_boot.py --dev_bdf 02:00.0 --fw fw2.bin
    Ex. python pcie_boot.py --dev_bdf 02:00.0 --fuser fuser2.bin

## Slide 4: Architect
/sys/bus/pci/devices/0000:01:00.0/resource0
libtemp_mmap.so
mmap, read / write(u32)
create libtemp_mmap.so 및 read / write call using ctype module
wrapper_mmap.py
pcie_boot.py
mmap filepath, command value, offset, data value
setpci 커맨드 실행 및 argument parser 추가

## Slide 5: Get Register
NVME device를 탐색하고 해당 device와 mmap을 수행
  NVME device 탐색 경로
    /sys/bus/pci/devices/0000: '01:00.0' /resource0
/sys/bus/pci/devices/0000:01:00.0/resource0
bar(addr)

## Slide 6: Load fw fuser nvme_ddr image
fw.bin, fuser.bin nvme_ddr.bin image를 읽고 buffer에 기록함
fw.bin
fw_buf
fw.bin
Image
fuser.bin
fuser_buf
fuser.bin
Image
nvme_ddr.bin
ddr_buf
nvme_ddr.bin
Image
fw_len
fuser_len
ddr_len
Host Memory

## Slide 7: Set Addresses
① ddr_raw_buf_addr = 0x8070008000
② fuser_raw_buf_addr = ③ jump_addr = 0x70000000
④ fw_raw_buf_addr = 0x8400000000
cmd_reg_addr
bar(addr)
0x50
offset
cmd_reg
cpl_reg
data_reg_addr
cpl_reg_addr
0x4(32bit)
0x4(32bit)
0x4(32bit)
data_reg
PMU
ROM Code

## Slide 8: Download ddr.bin (#1. Set address)
__set_cpl_reg(val)
  val 값이 cpl_reg_addr에 write 되도록 수행
  cpl_reg_addr = val ( DEFAULT_CPL_VAL(1) )
  __wait_cpl(val)
__wait_cpl(req)
  req 값이 cpl_reg_addr에 write 될 때까지 Spin
cmd_reg_addr
bar(addr)
0x50
offset
cmd_reg
(1<<28)
cpl_reg
(DEFAULT_CPL_VAL)
data_reg_addr
cpl_reg_addr
0x4(32bit)
0x4(32bit)
0x4(32bit)
data_reg
(addr_low)
__set_addr(type, addr_high, addr_low)
  write 하려는 buf의 address를 설정함
  __set_cpl_reg(DEFAULT_CPL_VAL)
  *data_reg_addr = addr_low
  *cmd_reg_addr = 1(0001) << 28
  __wait_cpl(PCIE_BOOT_STATUS_OK)
  __set_cpl_reg(DEFAULT_CPL_VAL)
  *data_reg_addr = addr_high
  cmd_reg_addr |= 1 (Address high)
  __wait_cpl(PCIE_BOOT_STATUS_OK)

## Slide 9: Download ddr.bin (#2. Set length)
__set_length(type, len)
  write 하려는 buf의 length를 설정함
  __set_cpl_reg(DEFAULT_CPL_VAL)
  *data_reg_addr = len
  *cmd_reg_addr = 2(0010) << 28
  __wait_cpl(PCIE_BOOT_STATUS_OK)
cmd_reg_addr
bar(addr)
0x50
offset
cmd_reg
(2<<28)
cpl_reg
(DEFAULT_CPL_VAL)
data_reg_addr
cpl_reg_addr
0x4(32bit)
0x4(32bit)
0x4(32bit)
data_reg
(len)

## Slide 10: Download ddr.bin (#3. Send data)
__send_data(type, buf, len_dw)
  buf 를 write 함, for 문으로 아래의 루틴을 수행
    __set_cpl_reg(DEFAULT_CPL_VAL)
    *data_reg_addr = buf + dw_cnt
    *cmd_reg_addr = 3(0011) << 28 | dw_cnt * bytes_per_dw(4)
    __wait_cpl(PCIE_BOOT_STATUS_OK)
  __set_cpl_reg(DEFAULT_CPL_VAL)
cmd_reg_addr
bar(addr)
0x50
offset
cmd_reg
(3<<28)
cpl_reg
(DEFAULT_CPL_VAL)
data_reg_addr
cpl_reg_addr
0x4(32bit)
0x4(32bit)
0x4(32bit)
data_reg
(buf + dw_cnt)
nvme_ddr.bin
Image
0x8070008000

## Slide 11: Set Addresses
① ddr_raw_buf_addr = 0x8070008000
② fuser_raw_buf_addr = ③ jump_addr = 0x70000000
④ fw_raw_buf_addr = 0x8400000000
cmd_reg_addr
bar(addr)
0x50
offset
cmd_reg
cpl_reg
data_reg_addr
cpl_reg_addr
0x4(32bit)
0x4(32bit)
0x4(32bit)
data_reg
PMU
ROM Code

## Slide 12: Execute fuser (#1. Set address)
cmd_reg_addr
bar(addr)
0x50
offset
cmd_reg
(C<<28)
cpl_reg
(DEFAULT_CPL_VAL)
data_reg_addr
cpl_reg_addr
0x4(32bit)
0x4(32bit)
0x4(32bit)
data_reg
(addr_low)
__set_addr(type, addr_high, addr_low)
  jump 하려는 buf의 address를 설정함
  __set_cpl_reg(DEFAULT_CPL_VAL)
  *data_reg_addr = addr_low
  *cmd_reg_addr = C(1100) << 28
  __wait_cpl(PCIE_BOOT_STATUS_OK)
  __set_cpl_reg(DEFAULT_CPL_VAL)
  *data_reg_addr = addr_high
  cmd_reg_addr |= 1 (Address high)
  __wait_cpl(PCIE_BOOT_STATUS_OK)
fuser.bin
Image
PMU
ROM Code
0x70000000

## Slide 13: Execute fuser (#2. Jump address)
cmd_reg_addr
bar(addr)
0x50
offset
cmd_reg
(D<<28)
cpl_reg
(DEFAULT_CPL_VAL)
data_reg_addr
cpl_reg_addr
0x4(32bit)
0x4(32bit)
0x4(32bit)
data_reg
__jump_to_fuser()
  Ack 수행
  __set_cpl_reg(DEFAULT_CPL_VAL)
  *cmd_reg_addr = D(1101) << 28
  __wait_cpl(PCIE_BOOT_STATUS_OK)
PMU
ROM Code
fuser.bin
fuser.bin
Image
0x70000000

## Slide 14: Set Addresses
① ddr_raw_buf_addr = 0x8070008000
② fuser_raw_buf_addr = ③ jump_addr = 0x70000000
④ fw_raw_buf_addr = 0x8400000000
cmd_reg_addr
bar(addr)
0x50
offset
cmd_reg
cpl_reg
data_reg_addr
cpl_reg_addr
0x4(32bit)
0x4(32bit)
0x4(32bit)
data_reg

## Slide 15: Complete fw download
__complete_fw_download()
  Ack 수행
  __set_cpl_reg(DEFAULT_CPL_VAL)
  *cmd_reg_addr = D(1101) << 28
  __wait_cpl(0xdeadbeef)
cmd_reg_addr
bar(addr)
0x50
offset
cmd_reg
(D<<28)
cpl_reg
(DEFAULT_CPL_VAL)
data_reg_addr
cpl_reg_addr
0x4(32bit)
0x4(32bit)
0x4(32bit)
data_reg
PMU
ROM Code
fuser.bin
0x8400000000
fw.bin
Image
0x8070008000
nvme_ddr.bin
Image
dram init
fw_validate
fw_replace
fw_activate
ack 0xdeadbeef
fw.bin
Image
0x8400000000